## Slide 1
CCVN Monthly Report - Month 07
Date: 31st July 2026

## Slide 2
Content
1.
Network quality and trends
1.1.
Ticket classification
1.2.
Failure status
1.3.
Top alarms for each product line
1.4.
Top spare parts used in the month
1.5.
Service cost in the month
2.
Issues, actions & resolution progress tracking
2.1.
Audit program for quality control of charging stations and BSS
1.6.
SLA Performance
Notes: Agenda of the report.

## Slide 3
1. Network quality & trends

## Slide 4
1.1. Ticket classification: EVCS
Classification
Ticket q'ty
Sharing
Ticket rate
Disclaim
2,280
20.1%
9.0%
Hardware
1,700
15.0%
6.7%
Firmware / Software
3,087
27.3%
12.2%
No fault found
3,818
33.7%
15.1%
Undefined yet
433
3.8%
1.7%
Grand Total
11,318
100.0%
44.6%
Note: Ticket rate = Ticket Q'ty / Total Chargers on service (25,354 chargers).
Description of Disclaim — 2,276 tickets
Duplicated / wrong information
850 · 37.3%
Power & internet infrastructure
612 · 26.8%
Cleaning / maintenance
284 · 12.5%
User operation error
160 · 7.0%
Other reasons
235 · 10.3%
Power off / CB tripped
36 · 1.6%
Who owns the ticket — share of 11,318
20.1%
15.0%
27.3%
33.7%
Disclaim 20.1% — not ChargeCore
ChargeCore-owned 79.9% — 9,038 tickets
Data comments:
· No fault found is the largest group — 3,818 tickets (33.7%, rate 15.1%).
· Firmware / software is second — 3,087 tickets (27.3%, rate 12.2%)
· Hardware is 1,700 tickets (15.0%, rate 6.7%) — clearly lower than in June (1,813 tickets).
· Disclaim is 20.1% , mostly duplicated / wrong information (37.3%) and power & internet infrastructure (26.8%).
· Undefined yet is 3.8% (433 tickets) — the work to reclassify tickets is working.
Action: merge duplicate tickets automatically, and add a remote check before we send a technician.
Notes: EVCS ticket classification. 79.9% of tickets are ChargeCore-owned; no fault found is the biggest single bucket.

## Slide 5
1.1. Ticket classification: BSS
Classification
Ticket q'ty
Sharing
Ticket rate
Disclaim
3,607
21.8%
14.2%
Hardware
2,215
13.4%
8.7%
Firmware / Software
3,279
19.9%
12.9%
No fault found
6,053
36.6%
23.8%
Undefined yet
1,364
8.3%
5.4%
Grand Total
16,518
100.0%
65.0%
Note: Ticket rate = Ticket Q'ty / Total BSS on service (25,430 cabinets).
Description of Disclaim — 3,584 tickets
Power & internet infrastructure
938 · 26.0%
Duplicated / wrong information
676 · 18.7%
Cleaning / maintenance
642 · 17.8%
Other reasons
557 · 15.4%
User operation error
352 · 9.8%
Not installed / not accepted
241 · 6.7%
Who owns the ticket — share of 16,518
21.8%
13.4%
19.9%
36.6%
8.3%
Disclaim 21.8% — not ChargeCore
ChargeCore-owned 78.2% — 12,911 tickets
Data comments:
· Ticket rate reached 65.0% of the cabinet fleet — two thirds of all BSS units had at least one ticket this month.
· No fault found dominates — 6,053 tickets (36.6%, rate 23.8%), ahead of firmware / software 3,279 (19.9%).
· Hardware 2,215 tickets (13.4%) — mostly locks, sensors (see 1.3 and 1.4).
· Disclaim 21.8% : infrastructure 26.0%, duplicated / wrong info 18.7%, cleaning 17.8%.
· Undefined yet 8.3% (1,364) — more than twice the EVCS share; BSS classification needs to improve.
Action: the BSS SOP package (status: completed) and the reclassification of the 1,364 undefined tickets are both needed before we can trust the baseline.
Notes: BSS ticket classification. Ticket rate 65% of the fleet.

## Slide 6
1.2. Failure status: EVCS
Models
Charger q'ty on service
Failed chargers
Fail. rate
Failure ticket
Freq.
AC
7,936
842
10.6%
1,154
1.37
Core
3,177
957
30.1%
2,112
2.21
Coremini
4,424
1,405
31.8%
2,906
2.07
Kern
3,699
1,181
31.9%
1,853
1.57
Socket
6,118
695
11.4%
1,013
1.46
Total
25,354
5,080
20.0%
9,038
1.78
Failure rate by model — M2 → M7 (colour = severity)
M2
M3
M4
M5
M6
M7
Trend · vs M6
AC
6.3%
11.8%
13.6%
14.8%
14.8%
10.6%
▼ -4.2pt
Core
22.3%
24.1%
30.5%
32.3%
31.8%
30.1%
▼ -1.7pt
Coremini
30.0%
28.1%
31.5%
41.7%
39.4%
31.8%
▼ -7.6pt
Kern
40.4%
37.2%
43.5%
48.3%
41.8%
31.9%
▼ -9.9pt
Socket
8.7%
5.9%
8.8%
9.5%
10.0%
11.4%
▲ +1.4pt
Data comments:
· Overall EVCS failure rate is 20.0% (5,080 of 25,354 chargers), improved from 22.0% in June.
· Kern improved most — 31.9% from 41.8% in June - but is still the highest failure rate of all models.
· Coremini 31.8% (from 39.4%) and Core 30.1% (from 31.8%); Core still has the most repeat failures (freq 2.21).
· AC dropped to 10.6% from 14.8%.
· Socket is the only model getting worse — 11.4% from 10.0% in June, rising every month since M3.
Action: bring Core, Coremini, Kern below 25% by M9, using the new FW batch (expected in early September) + the fan / filter rework as the two main measures.
Notes: EVCS failure status. Fleet failure rate improved to 20.0%. Kern improved most, Socket is the only model rising.

## Slide 7
1.2. Failure status (cont.): EVCS
Position of each model — failure rate × repeat frequency (bubble = fleet size)
2.4
Repeat frequency →
1.2
fleet average 20.0%
fleet average freq 1.78
AC
10.6% · freq 1.37
Core
30.1% · freq 2.21
Coremini
31.8% · freq 2.07
Kern
31.9% · freq 1.57
Socket
11.4% · freq 1.46
0%
Failure rate →
45%
Top-right is worst: Core and Coremini fail often and keep coming back — this is a design or repair-quality problem. Kern fails as often but rarely comes back (freq 1.57), which suggests single component failures. AC and Socket are the more reliable half of the fleet.
Failure tickets in the month, by model
AC
1,154 tickets · 842 failed units
10.6% · freq 1.37
Core
2,112 tickets · 957 failed units
30.1% · freq 2.21
Coremini
2,906 tickets · 1,405 failed units
31.8% · freq 2.07
Kern
1,853 tickets · 1,181 failed units
31.9% · freq 1.57
Socket
1,013 tickets · 695 failed units
11.4% · freq 1.46
Notes: Ticket volume vs failure rate and repeat frequency by model - this replaces the old dual-axis chart.

## Slide 8
1.2. Failure status: BSS
Models
BSS q'ty on service
Failed cabinets
Fail. rate
Failure ticket
Freq.
BSS-06
17,916
6,922
38.6%
11,246
1.62
BSS-12
7,514
1,243
16.5%
1,665
1.34
Total
25,430
8,165
32.1%
12,911
1.58
Failure rate by model — M2 → M7
M2
M3
M4
M5
M6
M7
vs M6
BSS-06
0.0%
0.5%
3.6%
7.3%
11.9%
38.6%
▲ +26.7pt
BSS-12
0.0%
0.0%
0.0%
0.1%
0.6%
16.5%
▲ +15.9pt
Important note: part of the jump comes from a change in how we measure — automatic incident-ticket dispatch from VOMS for BSS went live in the period, so faults that never became tickets before are now all recorded. July is the first month with complete BSS data.
Data comments:
· Overall BSS failure rate is 32.1% (8,165 of 25,430 cabinets).
· Almost all failures come from BSS-06 — 6,922 of 8,165 failed cabinets, 11,246 tickets, 38.6% failure rate (11.9% in M6).
· BSS-12 is now visible too — 16.5% (1,243 cabinets). It has been in service only a short time, so keep tracking it.
· Repeat frequency rose to 1.58 (1.28 in June) — repair quality is getting worse, not only the number of faults.
· Fault mix is mechanical: locks, sensors(A0112, B6029 / C6029) — see 1.3 and 1.4.
Action: fix July as the BSS baseline and set the August target on repeat frequency (≤1.35) — that shows repair quality on its own, apart from the extra new tickets.
Notes: BSS failure status. Automatic ticket dispatch went live, so M07 is the first month with complete data.

## Slide 9
1.2. Failure status (cont.): BSS
Position of each model — failure rate × repeat frequency (bubble = fleet size)
2.4
Repeat frequency →
1.2
fleet average 32.1%
fleet average freq 1.58
BSS-06
38.6% · freq 1.62
BSS-12
16.5% · freq 1.34
0%
Failure rate →
45%
BSS-06 sits far to the right with the higher repeat rate: 17,916 cabinets in service, generating 11,246 tickets. BSS-12 is at a third of that rate and comes back less often — the newer generation is holding up better so far.
Failure tickets in the month, by model
BSS-06
11,246 tickets · 6,922 failed cabinets
38.6% · freq 1.62
BSS-12
1,665 tickets · 1,243 failed cabinets
16.5% · freq 1.34
What to fix first
· Locks & sensors on BSS-06 — highest volume and the same fault codes month after month.
Notes: BSS ticket volume vs failure rate; BSS-06 carries the whole load.

## Slide 10
1.3. Top alarms for each product line: EVCS
AC: Top 5 alarms
1,486 tickets
A0101
363 · 45.1%
B0207
149 · 18.5%
CONNECTION_LOST
83 · 10.3%
A2007
71 · 8.8%
A0113
44 · 5.5%
Core & Coremini: Top 5 alarms
6,213 tickets
C2405
883 · 15.7%
C0116
608 · 10.8%
C2006
593 · 10.5%
D1403
541 · 9.6%
A0112
425 · 7.5%
Kern: Top 5 alarms
2,365 tickets
C2405
426 · 20.3%
A0112
331 · 15.8%
A0401
301 · 14.3%
A0101
160 · 7.6%
CONNECTION_LOST
130 · 6.2%
AC — A0101 (High Temperature)
RCA: The charger is inside a box or cabinet, or in direct sunlight. The FW temperature limit is set too low.
Solution: Ask the customer to remove the box or cabinet, move the charger into shade, or install a roof cover. The FW will adjust the temperature limit — in internal testing now, to be sent to VGreen on 6 Aug 2026.
Core / Coremini — C0116 (Fan Failed)
RCA: The fan or the 24V power supply is broken. Dirty filters are blocking the airflow.
Solution: Replace the broken fan or the 24V power supply. Clean the filters, and check that the fans spin correctly.
AC - B0207 (DataMismatch)
RCA: FW bug: the charger sends the StartTransaction message many times, so its data no longer matches the server.
Solution: Short term: run the "reset" command to restart the board and stop it re-sending old messages. Long term: fixed in the next FW release — in internal testing now, to be sent to VG on 6 Aug 2026.
Kern - C2405 (Link communication line error)
RCA: Poor network connection (loose or unshielded cables). A fault on a nearby charger breaks the group link. Power cut, or Emergency Stop pressed.
Long-term solution: Replace unshielded wires with shielded cables. Repair the faulty chargers nearby to restore the group link. Tell site owners not to cut the power by hand.
Core/Coremini - C2405 (Link Comm Error)
RCA: False alarms, and no automatic reconnection. One offline charger breaks the whole group. Power cut, or E-Stop pressed.
Solution: FW 260421CCDCxxCore will fix these bugs (TQA 20/7-20/8/2026; pilot running since 9 July 2026).
Kern – A0112 (DoorAccessDetected)
RCA: Hardware: the door sensor or the latch is broken or loose. Software: false or duplicate alarms; waiting for the FW fix.
Solution: Replace the broken sensor or the lock mechanism. FW 260421CCDCxxKern will fix this (TQA date not set yet — waiting for VF; pilot running since 9 July 2026).
Notes: Top 5 alarms per product line with RCA and solution. Most fixes are in the July FW batch.

## Slide 11
1.3. Top alarms for each product line: BSS
BSS: Top 10 alarms — 15,897 tickets
A0112
3,649 · 23.0%
B6029
2,840 · 17.9%
C6029
2,123 · 13.4%
C6030
1,687 · 10.6%
B6022
1,234 · 7.8%
A0605
554 · 3.5%
B6000
496 · 3.1%
B6021
373 · 2.3%
B6003
320 · 2.0%
Concentration: the door / lock / sensor group (A0112, B6029, C6029, C6030, B6022) accounts for 11,533 tickets — 72.7% of the top 10. One mechanical redesign programme would cover almost three quarters of all BSS alarms.
Detailed RCA and Solution: Refer to Part 2 of this report.
Notes: BSS top 10 alarms; lock, sensor and door faults dominate.

## Slide 12
1.4. Top spare parts used in the month: EVCS
Top spare parts — usage chart (Top 5) & cost table (Top 10)
Source: Tickets export – Spare Parts Record, July 2026, matched to the Sheet1 cost list by material code; 20 rows with a placeholder quantity of 999 were excluded.
Data comments:
· AD-DC Power Module - Core 60/120/150 Kw has both the highest usage (560 units) and by far the highest cost ($303,416) in the month.
· HV Core V2.8 is 2nd in usage (221 units, $8,619).
Reasons for AD-DC Power Module failure
· Input Under Voltage. · Power module group check error.
Solution for reducing Power Module fails
· New FW to remove "Input Under Voltage" alarms by keeping the current stable when the voltage changes (it lowers the power) — TQA & pilot run in July 2026. · Do regular maintenance (cleaning).
Chart: EVCS – Top 5 Spare Parts by Usage Qty
| AD-DC Power Module | COREmini QT Screen (Excluded PCBA) | AC PCBA - AC 22Kw | HV Core V2.8 - Core 60/80/120/150Kw | AD-DC Power Module - Core 60/120/150 Kw
Usage Qty | 160 | 211 | 212 | 221 | 560
# | Material Name | Qty | Est. Cost (USD)
1 | AD-DC Power Module - Core 60/120/150 Kw | 560 | $303,416
2 | HV Core V2.8 - Core 60/80/120/150Kw | 221 | $8,619
3 | AC PCBA - AC 22Kw | 212 | $7,017
4 | COREmini QT Screen (Excluded PCBA) | 211 | $31,740
5 | AD-DC Power Module | 160 | $66,286
6 | DC Cooling Fan - Core mini 60/80Kw | 137 | $3,511
7 | DC Charging Cable - Core mini 60/80Kw | 128 | $31,006
8 | OCPP AC 7kw and AC 22Kw (New Version) | 126 | $2,269
9 | QT Board (Compatible with CORE, COREmini, Kern) | 98 | $5,460
10 | DC Cooling Fan - Core 120/150Kw | 88 | $2,029
Notes: Spare parts EVCS. July export from CCTS still pending; M6 figures kept as reference.

## Slide 13
1.4. Top spare parts used in the month: BSS
Top spare parts — usage chart (Top 5) & cost table (Top 10)
Source: Tickets export – Spare Parts Record, July 2026, matched to the Sheet1 cost list by material code; 20 rows with a placeholder quantity of 999 were excluded. Cost shows N/A where the part code has no match in the cost sheet.
Data comments:
· Battery Compartment Lock Sensor - Shengjiu has the highest usage (3,138 units) but costs only $1,569; the biggest cost is After-sales Module ZZ Gen 1 at $16,601 (1,302 units), then the Shengjiu gen3 lock at $10,739 (1,375 units).
· SD card is the most used part outside the lock and sensor group (176 units, $704). Back plate and ZhongZheng lock have no cost record.
Root cause — hardware quality
The current parts are not durable enough. Standard SD cards wear out too fast, and the mechanical locks cannot handle repeated daily use by customers.
Solutions [proposal to HQ]
· Switch to industrial-grade SD cards and heavy-duty mechanical locks. · Ask the supplier for a quality review, or find a more reliable supplier.
Chart: BSS – Top 5 Spare Parts by Usage Qty
| Back plate - Shengjiu lock | Battery Compartment Lock Sensor - SK ¦ BSS | After-sales Module ZZ - BSS Gen 1 | Battery Compartment Lock - Shengjiu gen3 ¦ BSS | Battery Compartment Lock Sensor - Shengjiu ¦ BSS
Usage Qty | 609 | 706 | 1302 | 1375 | 3138
# | Material Name | Qty | Est. Cost (USD)
1 | Battery Compartment Lock Sensor - Shengjiu ¦ BSS | 3138 | $1,569
2 | Battery Compartment Lock - Shengjiu gen3 ¦ BSS | 1375 | $10,739
3 | After-sales Module ZZ - BSS Gen 1 | 1302 | $16,601
4 | Battery Compartment Lock Sensor - SK ¦ BSS | 706 | $353
5 | Back plate - Shengjiu lock | 609 | $2.21
6 | SD card | 176 | $704
7 | Slot Control Board - BSS 6/12 Slot | 48 | $541
8 | Battery Compartment Lock - ZhongZheng ¦ BSS | 39 | $9.57$
9 | Battery compartment ¦ BSS | 34 | $750
10 | BSS-Power Supply Module | 24 | $1,022
Notes: Spare parts BSS. Lock sensors and SD cards are the biggest items; proposal to HQ on component quality.

## Slide 14
1.5. SLA performance by ASP, SE: EVCS
Overdue rate by ASP / SE — M2 → M7 (colour = severity vs the 5.0% target)
M2
M3
M4
M5
M6
M7
M7 total · ovd
EC
4.0%
1.3%
7.7%
12.9%
15.1%
10.0%
3,010 · 301
ES
5.0%
6.1%
10.2%
12.0%
10.8%
11.5%
4,105 · 471
ITS
2.5%
3.0%
4.5%
15.1%
19.5%
15.8%
2,366 · 374
SE
–
27.3%
5.6%
10.6%
3.1%
1,798 · 55
Workload vs overdue rate — M7 (who needs action first)
20%
Overdue rate →
0%
SLA target 5.0%
EC · 10.0%
3,010 tickets
ES · 11.5%
4,105 tickets
ITS · 15.8%
2,366 tickets
SE · 3.1%
1,798 tickets
0
Ticket volume →
5,000
Data comments:
· Overall trend: three of four ASPs improved in July after the June peak, and all four are still above the 5.0% target.
· ITS is now the worst — 15.8% (374 of 2,366), down 3.7pt from June and still the highest rate.
· EC improved most — 10.0% from 15.1%, and now carries 301 overdue tickets.
· ES handles the most tickets but got worse — 11.5% on 4,105 tickets.
· SE (in-house) improved — 3.1% from 10.6% in June.
Problems:
· Waiting for spare parts: technicians arrived on time but had to wait days for spare parts (fans, boards, modules).
· Human error: technicians fixed the charger but forgot to close the ticket on the app.
· System problems: tickets that were already fixed were re-opened by customers, or buried under duplicate tickets.
Solutions:
· Keep extra spare parts closer to the technician teams.
· Require technicians to close tickets on the app right after the repair.
· Automatically delete duplicate tickets.
4.4%
EC/ES/ITS avg: 12.1%
All avg: 10.6%
Notes: SLA by ASP and SE for EVCS. Heatmap shows the six-month direction, the map shows volume vs rate.

## Slide 15
1.5. SLA performance by ASP, SE: BSS
Overdue rate by ASP / SE — M2 → M7 (colour = severity vs the 5.0% target)
M2
M3
M4
M5
M6
M7
M7 total · ovd
EC
–
–
82.0%
34.9%
16.2%
4,517 · 733
ES
–
–
64.2%
45.4%
22.4%
4,433 · 992
ITS
–
–
–
35.4%
37.7%
34.1%
3,248 · 1,107
SE
–
–
–
9.2%
8.3%
13.4%
3,616 · 486
Workload vs overdue rate — M7 (who needs action first)
50%
Overdue rate →
0%
SLA target 5.0%
EC · 16.2%
ES · 22.4%
ITS · 34.1%
SE · 13.4%
0
Ticket volume →
5,000
Data comments:
· ITS has the worst rate in M7 — 34.1% (1,107 of 3,248), only slightly down from 37.7% in M6 and still far above every other partner.
· ES 22.4% (992 of 4,433) and EC 16.2% (733 of 4,517) — both improved sharply but stay far above target.
· SE is still the best but rose to 13.4% from 8.3% in June as its BSS volume grew from 880 to 3,616 tickets.
· Ticket volume jumped for every partner in July (automatic BSS ticket dispatch) — the limit now is team capacity, not only work discipline.
Problems:
· Technicians fixed the issue on time but forgot to close the ticket on the app.
· Delays caused by waiting for spare parts (locks, sensors, boards) to ship.
· Too many tickets arrive at once; technicians gave priority to car chargers over battery stations.
Solutions:
· Require technicians to close tickets on the app right after fixing the issue.
· Keep common spare parts (locks, sensors, boards) with the technician teams or at local hubs.
–
–
All avg: 21%
4,517 tickets
4,433 tickets
3,248 tickets
3,616 tickets
EC/ES/ITS avg: 23.2%
Notes: SLA by ASP and SE for BSS. ITS is worst at 40%; SE rising fast from a low base.

## Slide 16
1.5. SLA performance by CSE: EVCS
Overdue rate by CSE — M2 → M7 (sorted by M7 ticket volume)
M2
M3
M4
M5
M6
M7
M7 total · ovd
thuanlu
3.9%
4.0%
6.7%
7.4%
10.1%
8.5%
2,988 · 255
hungvu
2.1%
16.5%
4.4%
5.9%
10.9%
3.5%
1,807 · 64
khiemnguyen
5.6%
1.5%
9.3%
18.0%
19.2%
10.6%
1,261 · 134
dinhnguyen
3.9%
1.7%
6.3%
15.0%
18.6%
15.8%
1,145 · 181
chuongpham
5.5%
8.7%
12.9%
15.9%
6.9%
14.3%
923 · 132
daochu
4.1%
2.5%
8.5%
19.2%
27.2%
19.0%
895 · 170
qtuan
5.1%
8.5%
6.3%
12.5%
14.1%
9.2%
861 · 79
thailong
4.5%
7.2%
10.6%
14.4%
11.2%
12.2%
811 · 99
tienkieu
2.8%
1.0%
4.7%
14.6%
11.8%
14.8%
588 · 87
SUM
4.0%
6.7%
7.5%
12.0%
13.7%
10.6%
11,279 · 1,201
M6 → M7 change per CSE (hollow = M6, solid = M7; scale 0 – 30%)
thuanlu
10.1% → 8.5% (-1.6pt)
hungvu
10.9% → 3.5% (-7.4pt)
khiemnguyen
19.2% → 10.6% (-8.6pt)
dinhnguyen
18.6% → 15.8% (-2.8pt)
chuongpham
6.9% → 14.3% (+7.4pt)
daochu
27.2% → 19.0% (-8.2pt)
qtuan
14.1% → 9.2% (-4.9pt)
thailong
11.2% → 12.2% (+1.0pt)
tienkieu
11.8% → 14.8% (+3.0pt)
Data comments:
· The overdue rate in July came down to 10.6% (from 13.7% in June); 6 of 9 CSEs improved.
· Worst: daochu 19.0% (down from 27.2% but still the highest), dinhnguyen 15.8%, tienkieu 14.8%.
· Best: hungvu 3.5% then thuanlu 8.5% on the largest load (2,988 tickets) and qtuan 9.2%.
· khiemnguyen improved most — 10.6% from 19.2% in June.
Causes:
· Weak ASP management & ticket allocation → new tickets become overdue almost immediately.
· Heavy workload + not enough ASP staff → team overloaded.
Actions:
· On-site quality inspections (audits): each CSE audits ≥5 stations per week using the SOP checklist, worst stations first. The overdue rate may rise at first, but fixing the root cause gives a lasting improvement. [Ongoing by CSE]
· daochu needs a dedicated review this month — 19.0% is still the highest rate of all CSEs.
Notes: SLA by CSE for EVCS. Heatmap plus M6 to M7 change per CSE; daochu is the only one getting worse.

## Slide 17
1.5. SLA performance by CSE: BSS
Overdue rate by CSE — M2 → M7 (sorted by M7 ticket volume)
M2
M3
M4
M5
M6
M7
M7 total · ovd
thuanlu
–
–
–
0.7%
2.8%
14.6%
3,028 · 443
chuongpham
–
–
–
53.1%
21.4%
29.4%
2,018 · 594
hungvu
–
–
–
15.5%
17.4%
12.8%
1,833 · 234
khiemnguyen
–
–
–
82.5%
33.9%
9.7%
1,689 · 164
qtuan
–
–
–
28.8%
26.0%
18.5%
1,582 · 292
dinhnguyen
–
–
–
72.0%
41.2%
33.4%
1,446 · 483
tienkieu
–
–
–
75.8%
34.6%
23.4%
1,169 · 274
daochu
–
–
–
50.0%
75.9%
39.2%
868 · 340
duynguyen
–
–
–
23.8%
50.0%
21.4%
1,124 · 241
thailong
–
–
–
65.6%
46.8%
24.0%
1,055 · 253
SUM
–
–
–
38.9%
30.6%
21.0%
15,814 · 3,318
M6 → M7 change per CSE (hollow = June, solid = July; scale 0 – 80%)
thuanlu
2.8% → 14.6% (+11.8pt)
chuongpham
21.4% → 29.4% (+8.0pt)
hungvu
17.4% → 12.8% (-4.6pt)
khiemnguyen
33.9% → 9.7% (-24.2pt)
qtuan
26.0% → 18.5% (-7.5pt)
dinhnguyen
41.2% → 33.4% (-7.8pt)
tienkieu
34.6% → 23.4% (-11.2pt)
daochu
75.9% → 39.2% (-36.7pt)
duynguyen
50.0% → 21.4% (-28.6pt)
thailong
46.8% → 24.0% (-22.8pt)
Data comments:
· The overdue rate came down to 21.0% in July (from 30.6% in M6) while volume jumped from 3,411 to 15,814 tickets.
· Worst: daochu 39.2% (340 overdue), dinhnguyen 33.4% (483), chuongpham 29.4% (594 — the largest overdue count).
· Best: khiemnguyen 9.7% then hungvu 12.8%, and thuanlu 14.6% on the largest load (3,028 tickets).
· thuanlu got worse the most — 14.6% from 2.8% in June, on 5× the volume.
Causes:
Same as the EVCS analysis — weak ASP allocation and not enough staff. On BSS this is worse, because ticket volume jumped when automatic ticket dispatch went live.
Actions:
· Same as EVCS: set a clear repair-and-recheck plan, and find out why faults come back after repair. The overdue rate may go up at first as old faults are found, but fixing the real cause will bring it down for good. [Ongoing by CSE]
· Rebalance the BSS load away from daochu and dinhnguyen until their rates are back under 30%.
Notes: SLA by CSE for BSS. daochu 63.8% and dinhnguyen 44.2% are critical.

## Slide 18
MONTHLY SERVICE COST — M1 → M7 (USD)
Excluding payment for BSS (pending) · M7 estimated
Description
M1
M2
M3
M4
M5
M6
M7 (Est.)
I. COST COMPONENTS
Spare parts
166,084
151,470
214,359
250,301
234,757
357,447
325,889
Cost for ASP (excl. BSS payment)
106,963
109,106
88,856
99,833
109,995
112,758
122,590
Salary for SE
–
–
13,530
14,544
36,895
53,807
69,572
Grand Total (USD)
273,047
260,576
316,745
364,678
381,647
524,012
518,051 ▼ 1.2%
II. INSTALLED BASE ON CPO & UNIT COST
Charger Q'ty activated on CPO
17,685
18,384
18,946
19,687
20,398
20,769
20,031
BSS Q'ty activated on CPO
–
–
7,969
12,023
16,147
21,984
27,891
Total Q'ty on CPO
17,685
18,384
26,915
31,710
36,545
42,753
47,922
Cost / equipment — total ($)
15.44
14.17
11.77
11.50
10.44
12.26
10.81 ▼ 12%
COST MIX BY MONTH
Spare parts
ASP
SE salary
M1
M2
M3
M4
M5
M6
M7
If the pending BSS payment is included
Description
M3
M4
M5
M6
M7 (Est.)
BSS payment for ASP
21,400
48,432
79,231
124,121
196,264
Grand Total (USD)
338,146
413,110
460,878
648,133
714,360
Cost / equipment ($)
12.56
13.03
12.61
15.16
14.91
1.6. Service cost in the month
Notes: M7 service cost is 464,345 USD, down 11.4% versus M6 — the first drop in five months, driven entirely by lower spare-parts consumption, and cost per equipment reached its best level at 9.69 USD. Two watch items: SE salary is now 15% of total cost, and if the pending BSS payment to ASP is included the month would instead be 660,609 USD at 13.79 USD per equipment.

## Slide 19
2. Issues, actions & resolution progress tracking

## Slide 20
Audit program for quality control of charging stations and BSS
See the detailed file attached.

## Slide 21
Thank You
Jamie (CCVN)